## Slide 1: DTI Atlas Registration via 3D Slicer and DTI-Reg
Guido Gerig, UUtah
Martin Styner, UNC
Clement Vachet, UNC

## Slide 2: DTI Registration
This tutorial teaches you how
  Load DTI datasets & masks
  Perform a pair-wise registration to a prior atlas via DTI-Reg
    Affine transform and deformable transform
  Save the transformed images and the deformable transform

## Slide 3
Combining information from multiple images requires the geometric relationship between them to be known...
Concept of Registration

## Slide 4
aligned
Concept of Registration: Overlay of pair of images
misaligned

## Slide 5
Transformation for Image Registration
Choice of transformations (complexity of transformation, #degrees of freedom
depends on application).
credit: R. Szelisky, Computer Vision

## Slide 6
3D Transformations
Translation (3 DOF)
Rigid:
Trans & Rot (6 DOF):
Affine (12 DOF)
B-spline (deformable,
grid of control points)
Diffeomorphic (highly deformable,
smooth transformation, invertible)
Linear Transformations (invertible, low DOF):
Nonlinear, deformable transformations (high DOF):

## Slide 7: Co-registration: From linear to nonlinear
Linear registration (affine)
Nonlinear registration (diffeom.)
Example: Registration of #DTI to atlas template

## Slide 8: Atlas Building: Averaging registred FA images
raw
linear
nonlinear
Quality (sharpness) of atlas improves with deformable transformations.

## Slide 9: DTI Population Atlases
Definition of standard, normative space
Templates to become available to researchers
Neonate
1 year
2 year
Adult
Rhesus (15mo)

## Slide 10: Spatial Transformations of Diffusion Tensors
Warmer colors indicate higher anisotropy
Principal diffusion directions in anisotropic regions of a DT-MR image slice
James Gee, Department of Radiology University of Pennsylvania

## Slide 11: Rotation without DT Reorientation: Transform voxel grid, leave tensors
  Directional structure is lost.
  DTs orientations are no longer consistent with the anatomical structure of the image.
James Gee, Department of Radiology University of Pennsylvania

## Slide 12: Rotation with DT Reorientation
  DR·D·RT.
  Directional structure preserved.
  DTs orientations remain consistent with the anatomy.
James Gee, Department of Radiology University of Pennsylvania

## Slide 13: Affine Tensor Transformations (Alexander et al, MICCAI 1999)
For an affine transformation, , DF·D·FT?
No...
DF·D·FT
Original Tensor
Transformed Tensor
DR·D·RT
We wish to preserve the shape of the DTs.
But we must reorient them appropriately.
Require R that reflects reorientation due to F.
Decompose F into:
  Rigid rotation, R, and
  Deformation, U: F = R·U R = F ·(FT ·F)-1/2
Then reorient D using R: D’ = R·D·RT
Finite Strain Estimation

## Slide 14: Dataset
For this tutorial you will need DTI data files that can be found following this link : http://hdl.handle.net/1926/1759

## Slide 15: Start Slicer 4
Linux/Mac users :
Launch the Slicer
executable located in
the Slicer4 directory
Windows users :
Select StartAll ProgramsSlicer4.0.1Slicer
Or launch the Slicer executable from Slicer4 directory

## Slide 16: Loading DTI Atlas
Left click on file menu
Left click on Add Volume

## Slide 17: Loading DTI Atlas
Select the AdultAtlas.nrrd volume

## Slide 18: Loading DTI Atlas Mask
Load AdultAtlas_BrainMask.nrrd label map

## Slide 19: Adjust View
Adjust view to see both mask and atlas
Link all 3 viewers
Opacity change
1
2

## Slide 20: Loading 2nd DTI dataset
File Menu =>Add Volume (or see previous tutorial)
Directory: DiffusionDataset_Step2
Load dwiDataset_DTI.nrrd

## Slide 21: Loading DTI dataset mask
File Menu =>Add Volume (or use from previous tutorial)
DiffusionDataset_Step2
Load BrainMask
“LabelMap” checkbox

## Slide 22: Overlay DTI datasets
How can we check alignment?
Overlay the DTI images!
1
2
Select AdultAtlas for Foreground
Set Opacity to 0.5

## Slide 23: Overlay
Bad alignment: 2 separate corpus callosum

## Slide 24: Select DTI-Reg Module
Slicer modules
  Diffusion
  → Utilities
  → DTI-Reg
DTI-Reg: Pairwise DTI registration module
Notes: Under Welcome to Slicer
Go to Diffusion
Utilities -> DTIreg

## Slide 25: Volumes for Registration
Fixed Volume: Target of registration = AdultAtlas.nrrd
Moving Volume: Image to be transformed: dwiDataset_DTI
1
2

## Slide 26: Set Masks for Registration
Set Fixed Mask to Atlas Mask: AdultAtlas_BrainMask.nrrd
Set Moving Mask to dwiDataset Mask: dwiDataset_BrainMask.nrrd
1
2

## Slide 27: Set Transform to Affine
Set registration transform to Affine
Deformable Registration is performed in 2 steps: Affine followed by nonlinear.
Only if you have ANTS pre-installed => select it!

## Slide 28: Select Outputs
Create & rename volumes for output
Affinely registered DTI dataset
Affine transform
Apply to run & wait
1
2

## Slide 29: Registration
Several pairwise registration methods available.
DTI-Reg supports several registration methods based on normalized FA images:
    Affine, B-spline, Demons-variants from within Slicer
    ANTS as external call (necessitates ANTS installation)
Future versions will also support DTI-TK
  Registration based on full tensor.

## Slide 30: Affine Results
Select DTI-Reg result as background
Result: single corpus callosum, but fuzzy, insufficient registration

## Slide 31: Deformable Registration
Concept: Use affine registration as initialization for deformable registration:
Change moving volume to affinely registered data
Change moving mask to atlas mask
Change registration to Diffeomorphic (Demons)
Create/rename output names for deformable transformation
1
3
5
2
4

## Slide 32: Deformable Results
Select DTI-Reg deformable result as background
Result: No longer fuzzy, significantly better registration

## Slide 33: Save Outputs and Done
Save selected volumes and transforms
File → Save → (deselect/select checkboxes)
Choose common directory: “destination for all selected”

## Slide 34: Conclusions
DTI registration is available in Slicer
2-step process currently, to be improved soon
Brainmasks are needed (unless data is skull stripped already)
This tutorial taught you how to register to an atlas
  Next step: how to use the atlas for fiber base analysis

## Slide 35: Acknowledgment
National Alliance for Medical Image Computing NIH U54EB005149
UNC: Jean-Baptiste Berger, Clement Vachet, Aditya Gupta
Utah: Guido Gerig, Sylvain Gouttard
Iowa: Hans Johnson, Joy Matsui