## Slide 1: Diffusion MRI Analysis
Sonia Pujol, Ph.D.
Zora Kikinis, Ph.D.
Harvard University, Boston, USA

## Slide 2: Tutorial Outline
This tutorial is an introduction to the fundamentals of Diffusion MRI analysis, from the estimation of diffusion tensors to the interactive 3D visualization of fiber tracts.
Diffusion MRI Analysis

## Slide 3: Tutorial Dataset
The tutorial dataset DiffusionMRI_tutorialData is a Diffusion Weighted MR scan of the brain acquired with 41 gradient directions and one baseline.
Diffusion Sensitizing Gradients
Diffusion Weighted Images (DWI)
Diffusion MRI Analysis

## Slide 4: Tutorial Software
The tutorial uses the 3DSlicer version 4.3
software available at www.slicer.org
Disclaimer
It is the responsibility of the user of 3DSlicer to comply with both the terms of the license and with the applicable laws, regulations and rules. Slicer is a tool for research, and is not FDA approved.
Diffusion MRI Analysis

## Slide 5: 3DSlicer software
An end-user application for image analysis
An open-source environment for software development
A software platform that is both easy to use for clinical researchers and easy to extend for programmers
3D Slicer is a multi-institution effort supported by the National Institutes of Health.
Diffusion MRI Analysis

## Slide 6: Part 1: From DWI images to Tensors
Diffusion MRI Analysis

## Slide 7: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
First, start Slicer4

## Slide 8: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
In your files archive, locate the file dwi.nhdr in the dataset folder for this tutorial

## Slide 9: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Drag and drop the file dwi.nhdr onto the viewer of the Slicer4 application

## Slide 10: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Exit the archive folders window, and click OK to load the dataset to Slicer

## Slide 11: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Slicer displays DWI volume of the brain

## Slide 12: Main Application Graphic User Interface (GUI)

## Slide 13: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Modules menu and select the module Volumes

## Slide 14: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Adjust the Window Level editor presets with the Volume module menu

## Slide 15: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position your mouse over the pin icon, then click on the link icon and the fit image to window icon

## Slide 16: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Slicer layout menu and select the Red slice only layout

## Slide 17: Loading the DWI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Slicer displays only the Axial anatomical slice in the Viewer

## Slide 18
Estimation of the tensors from diffusion weighted image
Diffusion Weighted Image Diffusion Tensor Image
(DWI) (DTI)

## Slide 19: From DWI to DTI
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Modules menu and select the module DWI to DTI Estimation

## Slide 20: From DWI to DTI
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module DWI to DTI Estimation in the modules menu:
-select the Input DWI volume ‘dwi’
-select Output DTI Volume ‘Create and Rename New Volume’, and rename it ‘dti’
-select Output Baseline Volume ‘Create and Rename new Volume’, and rename it ‘baseline’
-select the Estimation Parameter ‘LS’ (Least Squares) and click on Apply.

## Slide 21: From DWI to DTI
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position your mouse over the pin icon and select the volume dti

## Slide 22: From DWI to DTI
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Slicer displays the DTI volume in color by orientation mode:
Red: right-left
Green: anterior-posterior
Blue: inferior-superior

## Slide 23: Exploring the DTI Dataset
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Use the slider to browse through the dti volume, and try to locate the Corpus Callosum

## Slide 24: Corpus Callosum
The corpus callosum is a broad thick bundle of dense myelinated fibers that connect the left and right hemisphere. It is the largest white matter structure in the brain
Image from Gray’s Anatomy
Diffusion MRI Analysis

## Slide 25: Corpus Callosum
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Corpus Callosum

## Slide 26
Scalar measurements of diffusion tensor
from DTI to FA

## Slide 27: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Modules menu and select the module Diffusion Tensor Scalar Measurements

## Slide 28: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Fill in the following information:
-Set Input DTI Volume to ‘dti’
-Select Output Scalar Volume ‘Create new Volume’ and rename it ‘fa’
-Select the Operation ‘Fractional Anisotropy’
-Click on Apply to calculate the Fractional Anisotropy map of the tensor volume

## Slide 29: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
The FA image appears in the red viewer

## Slide 30: Fractional Anisotropy
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the Slicer layout menu and select Conventional layout

## Slide 31: Part 2: Tractography
Diffusion MRI Analysis

## Slide 32
Tractography seeded from
a region of interest (ROI)

## Slide 33: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position your mouse over the pin icon, click on << icon and change the Foreground to ‘None’ and the background to ‘fa’

## Slide 34: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module Editor

## Slide 35: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select Apply when the ‘label-map window’ appears,
then switch to the Yellow slice only layout

## Slide 36: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the fit to screen icon to adjust the dimensions of the yellow slice viewer to fit the screen

## Slide 37: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the DrawEffect tool

## Slide 38: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Outline the contour of the Corpus Callosum with the DrawEffect tool equipped and press enter. Repeat this step with 3 adjacent sagittal slices

## Slide 39: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
The tracts will be seeded from the region of interest (ROI) defined in the Corpus Callosum area.

## Slide 40: Diffusion MRI tractography
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module Tractography Label Map Seeding

## Slide 41: Labelmap Seeding: I/O
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
-Set the Input DTI Volume to ‘dti’
-Set the Input Label Map to ‘fa-label’
-Set Output Fiber Bundle to ‘Create and Rename New Fiber Bundle’ and rename it ‘corpusCallosum’

## Slide 42: ROI Drawing
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Under Seed Placement Options, check off the option for ‘Use Index Space’

## Slide 43: Labelmap Seeding: parameters
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the default Tractography Seeding parameters:
-Minimum Path Length: 10 mm
-Maximum Length: 800 mm
-Stopping Criteria: FractionalAnistropy
-Stopping Value: 0.15
-Stopping Track Curvature: 0.8
-Integration Step Length: 0.5 mm
Click on Apply

## Slide 44: Labelmap Seeding: parameters
Click on the Slicer layout menu and select Conventional layout

## Slide 45: Labelmap Seeding: Tracts
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
The tracts generated in the corpus callosum area appear in the 3D viewer.

## Slide 46: Tractography Results
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position the mouse over the pin icon and click on the eye icon to display the axial slice in the 3D viewer

## Slide 47
Tractography seeded from a fiducial

## Slide 48: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Select the module Mark Ups

## Slide 49: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the arrow icon to create a fiducial

## Slide 50: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position the fiducial in the left cingulum of the coronal slice

## Slide 51: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Double click on the fiducial and change the name to LeftCingulum
Set fiducial scale to 5.00

## Slide 52: Fiducial Seeding
Diffusion MRI Analysis
Select the module Tractography Interactive Seeding
Select the Input DTI volume ‘dti’
Select the Input Fiducials, Model or Label Map ‘F’
Select the Output Fiber Bundle ‘Create New Fiber Bundle’ and rename it ‘Cingulum’

## Slide 53: Fiducial Seeding
Diffusion MRI Analysis
Set the tractography parameters as follows:
-Fiducial region size: 2.5 mm
-Fiducial Seeding Step Size: 1.0 mm
-Maximum number of seeds: 100
-Minimum Path Length: 10 mm
-Maximum Path Length: 800 mm
-Stopping Criteria: Fractional Anisotropy
-Stopping Value: 0.15
-Stopping Track Curvature: 0.8
-Integration step length: 0.5 mm
-Create Tracts Initially as Tubes

## Slide 54: Fiducial Seeding
Diffusion MRI Analysis
Part of the left cingulum appears in the 3D viewer.
Move the Left Cingulum fiducial to explore the spatial relationship between the left cingulum and the corpus callosum

## Slide 55: Fiducial Seeding
Diffusion MRI Analysis
Go to the Markups module

## Slide 56: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Click on the arrow icon to create a second fiducial

## Slide 57: Fiducial Seeding
Image Courtesy of Dr. Alexandra Golby, Brigham and Women’s Hospital, Boston, MA..
Diffusion MRI Analysis
Position the fiducial in the right cingulum of the coronal slice

## Slide 58: Fiducial Seeding
Diffusion MRI Analysis
Part of the left and right cingulum appear in the 3D viewer.
Move the fiducials to explore the spatial relationship between the left and right cingulum, and the corpus callosum

## Slide 59: Tractography ‘on-the-fly’
Diffusion MRI Analysis
The Fiducial Seeding functionality allows you to do tractography ‘on-the-fly’ to explore white matter structures interactively

## Slide 60: DTI Analysis
Diffusion MRI Analysis
Select the module Data to display the list of elements that have been generated in this tutorial

## Slide 61: Conclusion
This tutorial guided you through the different steps of a Diffusion MR Analysis pipeline, from tensor estimation to 3D tracts visualization. This can be applied to explore and to study the fiber tracts of brain white matter .
Diffusion MRI Analysis – Sonia Pujol, Ph.D.
NA-MIC ARR 2012

## Slide 62
Contact: spujol@bwh.harvard.edu
zora@bwh.harvard.edu
Diffusion MRI Analysis – Sonia Pujol, Ph.D.
NA-MIC ARR 2012

## Slide 63: Slicer Community
www.slicer.org
Mailing lists:
slicer-user@bwh.harvard.edu
slicer-devel@bwh.harvard.edu
Diffusion MRI Analysis – Sonia Pujol, Ph.D.
NA-MIC ARR 2012
Notes: Download / update software
Find tutorials,
Give feedbaack, get help,
Find documentation

## Slide 64: Acknowledgments
Diffusion MRI Analysis
National Alliance for Medical Image Computing (NA-MIC)
NIH U54EB005149
Neuroimage Analysis Center (NAC)
NIH P41RR013218
Parth Amin, WIT ’16
Matthew Flynn, WIT ‘16