## Slide 1: 3D Slicer Workshop – University of Iowa DICOM Support for Quantitative Imaging
David Clunie (dclunie@dclunie.com)
PixelMed Publishing

## Slide 2: Learning Objectives
A few definitions
A brief history
Some justification
Why doing more than the least is better
What to encode
How to encode it
What is new and useful
How to package it all together

## Slide 3: What is Quantitative Imaging?
“Quantitative imaging is the extraction of quantifiable features from medical images for the assessment of normal or the severity, degree of change, or status of a disease, injury, or chronic condition relative to normal … includes the development, standardization, and optimization of anatomical, functional, and molecular imaging acquisition protocols, data analyses, display methods, and reporting structures … permit the validation of accurately and precisely obtained image-derived metrics with anatomically and physiologically relevant parameters, including treatment response and outcome, and the use of such metrics in research and patient care.”
RSNA QIBA
“https://www.rsna.org/QIBA.aspx”

## Slide 4: What is Quantitative Imaging?
“Quantitative imaging is the extraction of quantifiable features from medical images for the assessment of normal or the severity, degree of change, or status of a disease, injury, or chronic condition relative to normal … includes the development, standardization, and optimization of anatomical, functional, and molecular imaging acquisition protocols, data analyses, display methods, and reporting structures … permit the validation of accurately and precisely obtained image-derived metrics with anatomically and physiologically relevant parameters, including treatment response and outcome, and the use of such metrics in research and patient care.”
RSNA QIBA
“https://www.rsna.org/QIBA.aspx”

## Slide 5: What is DICOM?
Digital Imaging and Communications in Medicine
  “Facilitates interoperability of devices claiming conformance
  Addresses semantics of commands & associated data
  Addresses semantics of file services, file formats & information directories for off-line communication
  Explicit in defining conformance requirements …
  Facilitates operation in a networked environment.
  Structured to accommodate the introduction of new services … facilitating support for future medical imaging applications.”
  DICOM PS3.1 Introduction & Overview
  “http://dicom.nema.org/medical/dicom/current/”

## Slide 6: DICOM – Brief History
1982 – 1st PACS Conference – session on standards
1982 – AAPM Report 10 – Standard Format for Image Interchange
1983 – ad hoc meeting between FDA, ACR & NEMA
1983 – 1st meeting of ACR-NEMA “Digital Imaging and Communications Standards” Committee
1985 – ACR-NEMA 300-1985 (“version 1.0”) issued
1988 – ACR-NEMA 300-1988 (“version 2.0”) issued
1990 – Inter-vendor testing of version 2.0 at Georgetown
1992 – Trial of DICOM (“version 3.0) at RSNA
1993 – DICOM 3.0 issued

## Slide 7: DICOM – Brief History
1982 – 1st PACS Conference – session on standards
1982 – AAPM Report 10 – Standard Format for Image Interchange
1983 – ad hoc meeting between FDA, ACR & NEMA
1983 – 1st meeting of ACR-NEMA “Digital Imaging and Communications Standards” Committee
1985 – ACR-NEMA 300-1985 (“version 1.0”) issued
1985 – IEEE 802.3 Ethernet (based on 1976 Metcalfe)
1986 – Aldus TIFF (version 3; prior versions drafts only)
1987 – CompuServe GIF
1988 – ACR-NEMA 300-1988 (“version 2.0”) issued
1990 – Inter-vendor testing of version 2.0 at Georgetown
1992 – Trial of DICOM (“version 3.0) at RSNA
1992 – JPEG (ITU T.81; ISO 10918-1 1994)
1993 – DICOM 3.0 issued

## Slide 8: DICOM – Brief History
ACR-NEMA versions 1 and 2
  50-pin 16 bit parallel interface
  no network (assumed “network interface unit”)
  layered
  messages with commands and data
  tag-value pairs
  described patients, studies, images
  described modality, acquisition, 3D position, etc.

## Slide 13: DICOM – Brief History
ACR-NEMA versions 1 and 2
  50-pin 16 bit parallel interface
  no network (assumed “network interface unit”)
  layered
  messages with commands and data
  tag-value pairs
  described patients, studies, images
  described modality, acquisition, 3D position, etc.
DICOM “3.0”
  TCP/IP network protocol (and OSI semantics)
  “object-oriented” description & conformance

## Slide 14: DICOM – Scope
Implicit in the standard’s name: “Digital Image and Communications in Medicine”
Images and image-related information
All acquisition modalities (all “’ologies”)
  1993: CR, CT, MR, US, NM, SC (DF and DV)
  2014: XA, XRF, DX, MG (+DBT), IO, PT, VL (Photo, Endo, Slide), WSI, OCT (OP,IV)
  RT, SR (+CAD), waveforms, OP measurements and maps, surface scans, implants, segmentations
Storage + other services

## Slide 15: Why does DICOM exist ?
Previous solutions closed (proprietary)
Real world requires open standards
  heterogeneous modalities
  heterogeneous workstations
  heterogeneous archives, PACS, etc.
Consortium of
  industry (NEMA)
  users (ACR, ACC, CAP ...)

## Slide 16: Why (open) standards at all ?
Too many permutations of ...
  Acquisition device vendors
    general
      GE, Siemens, Philips, Toshiba, Shimadzu, Hitachi, ...
    special
      Bruker, iTheraMedical, Mediso, PerkinElmer ...
  Processing and archive device vendors
    general
      GE, Siemens, Philips, ... (+ open source)
    special
      NeuroQuant, InViCRO, ...

## Slide 17: Why not “existing” standards ?
Didn’t “exist” when ACR-NEMA formed
Pure imaging standards (TIFF, etc.)
  limited support for medical image types
  don’t encode domain specific information
Other domains not a good fit
  military, remote sensing, astronomical, etc.
ISO standards (e.g., IPI) never adopted
Medical standards that didn’t do images
  HL7, MIB (IEEE 1073), etc.
Needed more services than just storage
  query/retrieve, printing, workflow, etc.

## Slide 18: DICOM – Why?
Domain-specific fields
  patient identification & characteristics
  device identification & characteristics
  acquisition protocol parameters
  study management identifiers, dates and times
Need to handle binary bulk pixel data
  e.g., HL7 text based and no image support
Need to be extensible
  evolving technology, private extensions
  variable rather than “fixed” length headers

## Slide 19: Key goals of DICOM
Support interoperability
  NOT (necessarily) interfunctionality
  WITHOUT defining (restricting) architecture
Define conformance
  specific services and objects
  documentation (Conformance Statement)
  negotiation
Consensus standard
Voluntary compliance
Open (license fee free)

## Slide 20: DICOM – Modality Interface
Modality
Archive
Modality
Modality
Modality
PACS +/- RIS
Manager
Workstations
Standard Boundary

## Slide 21: DICOM - Workstation Interface
Modality
Archive
Modality
Modality
Modality
PACS +/- RIS
Manager
Workstations
Standard Boundary
Standard Boundary

## Slide 22: DICOM - Workstation Interface
Modality
Archive
Modality
Modality
Modality
PACS +/- RIS
Manager
Workstations
Standard Boundary
Standard Boundary
Bidirectional !

## Slide 23: DICOM & Quantitative Imaging
Encoding of images & results
Terminology & codes
DICOM standards in clinical practice
  images from modalities
  derived images – e.g., CBF
  ROIs – e.g., CT Hounsfield units, PET SUV
  size measurements – distance, area, volume
“Quantitative” imaging is nothing new
  different emphasis than narrative reporting

## Slide 24: Clinical v Research Use Cases
Narrative reporting
  see it, compare it, dictate it
Quantitative reporting +/- research
  see it, analyze it, measure it, code it, re-use it
Same standards
  greater need for numbers & codes
  more structure

## Slide 25: See It, Compare It, Dictate It
“Hairy mass, rt. temporal lobe, bigger”

## Slide 26: See It, Analyze It, Measure It
Segmented Lesion Volume 31,524 mm3

## Slide 27: Code It
Why, how, what, where …
(R-F8106,SRT, “Grand mal seizure”)
(24587-8,LN,“MR brain w/wo IVC”)
(F-04E4E,SRT,“Brain mass lesion”)
(RID6061,RADLEX, “Circumferential enhancement”)
(T-A250D,SRT,“Right Temporal Lobe)

## Slide 28: Tabulate It
Lesion # | TimePoint # | Volume | Auto LD | Auto SD | % From Baseline Volume
1 | 20020501 | 24120 | 57 | 27 | 0
1 | 20020827 | 43990 | 58 | 31 | 82
1 | 20020919 | 31524 | 46 | 37 | 31
1 | 20021026 | 31554 | 59 | 35 | 31
1 | 20021207 | 27081 | 49 | 27 | 12
1 | 20030219 | 39748 | 55 | 37 | 65

## Slide 29: Graph It

## Slide 30: Aggregate It and Visualize It

## Slide 31: Re-Use It
Quantitative analysis need not be a “dead end”
  can just transcribe or cut-and-paste numbers into a dictated or plain text report
  pre-populated “merge” fields created from structured input provide a productivity and quality gain
  can indeed save pretty tables & graphics as a screen shot or PDF
  but … much better to be able to re-use structure, numbers, codes next time, for comparison, searching, mining and basis for quality improvement metrics

## Slide 32: Preaching to the Converted
Researchers know this
But …
  don’t always use standards, or the same “standards” as their clinical colleagues
Why not?
  contempt for “outdated” format
  “not invented here” syndrome
  lack of convenience
  lack of familiarity
  lack of availability (in tools)
  missing features

## Slide 33: Preaching to the Converted
Researchers know this
But …
  don’t always use standards, or the same “standards” as their clinical colleagues
Why not?
  contempt for “outdated” format
  “not invented here” syndrome
  lack of convenience
  lack of familiarity
  lack of availability (in tools)***
  missing features***

## Slide 34: Changing the Paradigm
“Translational” research
  “bench to bedside” – compatibility with PACS
  co-clinical trials – animals + patients at same time
Improving the tools
  export capability in clinical formats from 3D Slicer
Improving the standard
  multi-frame images (one file for entire volume)
  quantitative images – real world values
  label maps, segmentations, parametric maps
  floating point pixels
  structured reports with numeric measurements

## Slide 35: Self-Serving Reasons
Data management problem
Missing metadata for identification/management
  project, acquisition (what)
  subject (who)
  history (when/where)
Manual approach
  files, folders, portable drives, sticks, spreadsheets
Managed non-standard approach
  metadata tags in proprietary database
Standard approach
  metadata preserved in file header, not detached,

## Slide 36: Composite Context
DICOM objects contain “composite context”
  Patient … same for all instances for patient
  Study … same for all instances for procedure
  Series … new for each acquisition/derivation
  Equipment
  Frame of Reference
Needs to be de-identified
  use research IDs to replace patient IDs, etc.
Research tools must preserve & propagate
  into derived objects (images, SEG, REG, SR, etc.)
  via intermediate objects (e.g., floating point parametric map, raw data instances)

## Slide 37: Quantitation – Images In
Modalities make DICOM images
  often do not populate critical attributes for quantitative imaging in a standard way
  anatomy, protocol, technique, contrast, timing
  workflow challenge – copy from modality work list
  user entry – need a place on screen, need to do it
  copy to header – sometimes standard lags behind
  evolving technology – need for private data elements
  inertia once implemented – delays standard elements
  quantitative pixel values – physical units & quantities
“Can lead a horse (vendor) to water (standard), but can’t make it drink”

## Slide 38: Enhanced Multi-frame Images
Per-frame attributes
Pixel data
Shared attributes

## Slide 39
Dataset (attributes+pixels)
C-Store response (acknowledgement)
C-Store request
UIDs
Store, parse, check
A s s o c i a t i o n
DB
DB
DB
DB

## Slide 41
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1
1 mm
2
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
1 mm
1897
Potentially thousands of individual per slice database insertion operations

## Slide 42
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1
1 mm
2
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
………..
……
1 mm
1897
Potentially thousands of individual per slice database insertion operations

## Slide 43
DB
PATIENT TABLE
0125678
Smith^James
0125735
Jones^Alan
………..
…………
STUDY TABLE
20051109
2267
20060301
3920
………..
……
SERIES TABLE
1
Localizer
2
Axial C/A/P
…
……
IMAGE TABLE
1 mm
1
Single database insertion - just don’t need per-slice detail in database

## Slide 44: Not (just) about performance
Greater “inter-functionality”
  browsing
  routing
  hanging
  rendering
Achieved through
  better description of organization of data
  more mandatory attributes
  more standard values (& codes)
  reduced dependence on private attributes

## Slide 45: MR Acquisition Contrast
Original SOP Classes
  guess from echo and repetition time, etc.
  recognize proprietary Protocol Name
Enhanced SOP Classes
  new mandatory frame level attribute
  Acquisition Contrast
    DIFFUSION, FLOW_ENCODED, FLUID_ATTENUATED, PERFUSION, PROTON_DENSITY, STIR, TAGGING, T1, T2, T2_STAR, TOF

## Slide 46: Technique Attributes & Terms
 | CT |  | MR | 
SOP Class | Original | Enhanced | Original | Enhanced
Attributes (Mandatory) | 18 (0) | 41 (39) | 44 (2) | 103 (94)
Terms (Enumerated) | 4 (2) | 86 (18) | 38 (9) | 228 (47)

## Slide 47: Hanging protocol rule impact
T1 SAG PRE GD
T1 AXIAL PRE GD
T2 AXIAL
T1 AXIAL POST GD
Acquisition Contrast = T1
Image Orientation ≈ 1\0\0\0\1\0
Contrast Agent #1
Administered = YES
Route = (G-D101,SNM3, “IV”)
Ingredient = (C-17800,SRT, “Gd”)

## Slide 48: Acquisition Timing Information
Original SOP Classes
  inconsistent use of
    Content (Image) Time
    Acquisition Time
    Frame Time (+/- Frame Time Vector)
  contrast timing information never used
Enhanced SOP Classes
  unambiguous definition of acquisition timing
  explicit relationships with contrast & cardiac timing

## Slide 49: Timing Information

## Slide 50: Cardiac Timing Information

## Slide 51: Organizational Features
Shared and Per-frame Functional Groups
  a Functional Group has Attributes that vary as a group
  e.g., Pixel Measures, Plane Orientation
  compact & makes explicit what doesn’t change
Dimensions
  a priori hints as to how the frames are organized
  specify intended order of traversal, such as space, then time (e.g., for cardiac cine loops)
Stacks
  groups of spatially-related slices, repeatable
Temporal positions
  “time slots” or “bins”

## Slide 52: Organizational Features
Goal is to reduce the work that the receiving application has to do to “figure out”
  how the data is organized
  why it is organized that way
Without preventing use of the data in unanticipated ways
  e.g. 3D on a dataset not intended as a volume
Two “levels”
  detailed: shared & per-frame attributes
  overall: dimensions, stacks and temporal positions

## Slide 53: Multi-frame Functional Groups
Per-frame attributes
Pixel data
Shared attributes

## Slide 54: What is a Functional Group?
“A set of logically related Attributes that are likely to vary together”
Examples:
  position related
  orientation related
  spacing related
  timing related
May be “shared” (all same) or “per-frame”
  Shared Functional Group Sequence – one item
  Per-Frame FGS – one item per frame (vector)

## Slide 55: Functional Group Encoding

## Slide 56: Functional Groups – Varieties
Common to many IODs, e.g.,
  Pixel Measures
  Frame Anatomy
  Frame VOI LUT
  Real World Value Mapping
Specific to particular IODs, e.g.,
  MR Spatial Saturation
  CT Table Dynamics
  X-Ray Field of View
  PET Frame Correction Factors
  US Image Description

## Slide 57: Modules vs. Functional Groups
Still have traditional “Modules” at top level
Modules
  Attributes describing entire acquisition
  e.g., cumulative stuff
Shared functional groups
  Attributes about frames that happen to have the same values for all frames
Per-frame functional groups
  Attributes about frames that have different values for any frame

## Slide 58: Stacks
H\

## Slide 59
5
Stack ID
In-Stack Position
1
3
4
1
2
3
4
2
5

## Slide 60: Multi-frame Dimensions
Real world (Wikipedia):
  “In physics and mathematics, the dimension of a space or object is informally defined as
    the minimum number of coordinates needed to specify any point within it”
DICOM:
  “A dimension is a set of attributes
    that change on a per-frame basis in a manner that is known before the image is acquired,
    are defined by the generating application and
    are especially intended for presentation”

## Slide 61: Multi-frame Dimensions
Multi-frame Dimensions Module
  in top level dataset
  defines an “organization” (set of dimensions)
    with an optional organization “type”
    e.g., “3D” or “3D_TEMPORAL” in Volume US
  defines each dimension
    by reference to a per-frame varying Attribute
    by referenced to Functional Group containing Attribute
For each frame, encode
  numeric “index” of position within each dimension
    starts from 1, increases by 1
    an index, not the value of the referenced Attribute

## Slide 62
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (2)
Time (1)
2
\
1
\
5
Dimension Index Values
Dimension Index Pointers:
Temporal Position Index
Stack ID
In-Stack Position
5
1\1\5
In-Stack Position
Stack ID = 1
4
1\1\4
3
1\1\3
2
1\1\2
1
1\1\1
5
2\1\5
In-Stack Position
Stack ID = 1
4
2\1\4
3
2\1\3
2
2\1\2
1
2\1\1

## Slide 63: But when ?
Modality
PACS

## Slide 64: Enhanced MF for Research
Few modalities create enhanced MF yet
  notable exceptions: Philips MR, Bruker MR
No reason not to “convert” legacy images
Benefits
  don’t have to manage hundreds of slice files
  don’t lose metadata converting to research-specific volume-oriented format (e.g., NRRD, NIfTI, Analyze, MNI, etc.)
How?
  convert generic stuff that all vendors do
  +/- retain/convert (relevant) private attributes
  specific supplement (157) to DICOM to describe it

## Slide 65: Legacy Converted Enhanced
“True” Enhanced MF objects in DICOM
  many mandatory required attributes/values
  one of their benefits, if information is known
  hard to populate during conversion
Legacy Converted Enhanced MF objects
  mandatory conversion of geometry (position, orientation, spacing)
  optional conversion of other generic stuff, if known
  sequences to store all other original attributes, separated into shared and per-frame sets
  specific variants for CT, MR and PET
Enhanced Secondary Capture MF family
  grayscale or color
  may include geometry and other functional groups

## Slide 66: PACS to PACS (or VNA) with Legacy DICOM Object Conversion
Modality
Modality
Workstations
PACS
Convert SF -> MF
Convert MF -> SF
Classic SF
Legacy Converted MF
True Enhanced MF
PACS
Convert SF -> MF
Convert MF -> SF

## Slide 67: Measurements Out
Regions of Interest (ROI)
  contours and other image-related references
  measurements, categorical assessments
Per-voxel values
  parametric maps (e.g., SUV, ktrans)
  label maps and segmentations
Intermediate re-usable work products
  spatial registration (rigid & deformable)
  fiducials
  real-world values (quantities & physical units)

## Slide 68: DICOM encoding of ROIs
Private elements
  evil & must be stopped
Curves in image
  weak semantics, old, retired
Overlays in image
  weak semantics
Presentation States
  weak semantics, PACS favorite
Structured Reports
  best choice, but more work
RT Structure Sets
  coordinates only
Segmentations
  per-voxel ROIs; use with SR
Date | Volume | Auto LD | Auto SD
20021207 | 27080 | 49 | 27
… | … | … | …

## Slide 69: DICOM Structured Reports
Hierarchical structure
  codes, numbers, coordinates, image references, etc.
Flexibility is constrained by templates
  just as XML is constrained by DTD or Schema
Standard DICOM binary representation
  easily stored in PACS though general purpose visualization remains challenging
  easily transcoded to XML or JSON for processing
Widely used in existing quantitative modalities
  echo-cardiography, obstetric ultrasound
  received and understood by voice reporting systems
Easier to implement if good toolkit support
  e.g., dcmtk provides abstractions in an SR API

## Slide 70: SR – Questions and Answers
Tree of nodes
Most nodes are name-value pairs
  name is the “question” (code)
  value is the “answer” (text, code, numeric, etc.)
Different style choices possible, e.g.
  (M-54000,SRT,“Necrosis”) = (G-A203,SRT,“Present”)
  (F-00005,SRT,“Finding”) = (M-54000,SRT,“Necrosis”)
Template of questions & value sets
  populated by human (pick lists from value sets)
  encode image processing results (e.g., detect signal)
  rule based (e.g., too small to measure)

## Slide 71: SR Templates for Quantitation
Described in DICOM PS3.16
  many existing templates for clinical quantitative applications, e.g., cardiovascular, OB/GYN
  good basis for research design, but insufficient
QIICR project proposed new templates
  accepted into DICOM as final text 2014/11
  root template for generic “imaging measurements” (CP 1386)
  reused recently added planar/volumetric ROIs as well as simple measurements
  re-used improved “image library” to describe relevant image characteristics acquisition parameters (CP 1389)
  added code sets for perfusion (CP 1391) and PET (CP 1392) methods and measurements
  shared definition of “quantities” with separate real world value map improvements

## Slide 72: Example of Measurement Report

## Slide 73: Example of PET Measurement - I

## Slide 74: Example of PET Measurement - II

## Slide 75: Example of Image Library

## Slide 76: Example of New Codes & Definitions

## Slide 77: DICOM RT Structure Sets
Simple structure
  focus is iso-contour 3D coordinates of regions to treat
  very limited semantics
  no standard/extensible measurements beyond volume
Standard DICOM binary representation
  easily transcoded to other DICOM objects like SR or PS if 3D (patient-relative) to 2D (image-relative) coordinate mapping is available (e.g., via source images or an SR image library)
Widely used in existing RT & non-RT systems
  also understood by many academic software tools

## Slide 78: DICOM Presentation States
Intended to preserve appearance
  grayscale pipeline (window)
  spatial transformation (pan/zoom)
  annotation (text, overlays, vector graphics)
Lack semantics
  what does the text “mean”? (NLP)
  which graphic is it associated with?
Overall, a poor choice for quantitative results
  may be all that is available in many PACS (to create & view)

## Slide 79: Parametric Maps
Foster N L et al. Brain 2007;130:2616-2635
Meyer P T et al. J Neurol Neurosurg Psychiatry 2003;74:471-478

## Slide 80: Label Maps
Brewer J et al. AJNR 2009; 30:578-580

## Slide 81: Parametric & Label Maps
Per-voxel encoding of numeric or label values
“Images”, but not just “pretty pictures”
  modality-specific or secondary capture; single or multi-frame
Segmentations (alternative to label maps)
  binary, probability, fractional occupancy
  multiple segments (multiple labels)
Parametric maps
  pixel value “means something” – real world value map (RWVM)
  integers +/- (linear) rescaling to floats (usable by any viewer)
  “derived” images of modality-specific SOP Class
  recently added floating point voxels and SOP Class (Sup 172)
Leave “fusion” (superimposition) to application
  e.g., PET SUV on top of CT
  can use Blending Presentation State to specify what to fuse

## Slide 82: Segmentations
Can be used to encode tissue segmentation, functional segmentation, and artifact identification for quantification or visualization
Can encode segmentation of entire volumes, single slices, smaller sub-regions, or 2D frames
An alternative mechanisms to encode ROI: voxel based, rather than contours (outlines)
Useful for encoding “atlases”
Coded description of segment category can be anatomical or property based or both
Encoded as a multi-frame image
Each frame represents a 2D plane or a slice of a single segmentation category

## Slide 83: Segmentation Codes

## Slide 84: Segmentations
More than one segment category is supported per instance – if more than one segment category is defined, each is encoded in a separate set of frames (i.e., multiple segment categories are not packed into pixels or indexed – not a numerical “label map”)
Segmentations are either binary or fractional (probability or occupancy percentages)
Spatial sampling and the extent do not need to be identical to the referenced images – need encode only region within “bounding box” of voxels in segments (subset of frames, subset of image matrix)
For 3D segmentations, related to patient coordinate system via Frame of Reference +/- explicit reference to images on which segmentation was performed

## Slide 85: DICOM Segmentation Example
Harvard Brain Atlas converted from NRRD Label Map with numerical voxel indices to DICOM Segmentation with one bitmap per anatomical segment, superimposed on differently sampled “original” MR image

## Slide 86: Parametric Maps
Each pixel value has "meaning" in real world
“Parametric" alludes to the meaning being the parameter of something, e.g.:
  parameters of pharmacokinetic models, such as Ktrans of the Tofts model used in DCE-MRI
  regional cerebral blood volume (RCBV) or flow (RCBF) used in perfusion CT
  normalized values based on body size, such as SUVbw used in PET
  diffusion parameters such as Apparent Diffusion Coefficient (ADC) used in MR DWI

## Slide 87: Parametric Maps
Can be encoded as:
  “traditional” IOD-specific images of “derived” type
  new Parametric Map Storage SOP Class
Parametric Map Storage SOP Class
  integer or floating point (32 or 64 bit) pixels
  single “sample” per frame (i.e., monochrome)
  pseudo-coloring for rendering defined separately
  leverages functional groups, dimensions, 3D positioning of enhanced MF family objects
  for intermediate files (to propagate composite context)
  uses Real World Value Map mechanism to define “meaning” of parameter values

## Slide 88: Real World Value Mapping
Value
Unit
Stored
Values
Real
Value
LUT
VOI
LUT
P
LUT
Display
Real world
value
Modality
LUT
Measurement
Units Code
Sequence
(0040,08EA)
Real World
Value LUT
Data
(0040,9212)
Real World
Value Intercept
and Slope
attributes
or

## Slide 89: Real World Value Mapping
Separate pipelines based on pixels
  what to show on the display
  what the pixel (voxel) “means”
e.g., MR pixel values
  signal intensity windowed for display
  mapped to physical unit (e.g. phase contrast velocity)
  recently added code for “quantity” as well (CP 1387)
Encoding options:
  within image or separate object (e.g., derived later)
  linear equation or LUT, applied to all/sub-set of range
  point operation (applies to all voxels in slice/frame)
  referenced from SR for ROI measurement (CP 1388)

## Slide 90: Real World Value Mapping
Units:
  Unified Code for Units of Measure (UCUM)
Quantity defined (extensibly) as:
  (G-C1C6, SRT, "Quantity”)
  (121401, DCM, “Derivation”)
  (G-C036, SRT, “Measurement Method”)
E.g., Cerebral Blood Flow (CBF)
  Measurement Units Code Sequence
    (ml/[100]g/min, UCUM, "milliliter per 100 gram per minute")
  Quantity Definition Sequence
    (G-C1C6, SRT, "Quantity") = (113055, DCM, "Regional Cerebral Blood Flow")

## Slide 91: Blending Presentation State
select superimposed
[register]
resample
within slices
between slices
select underlying
rescale and window
blend
pseudo-color

## Slide 92: Registration & Fiducials
Mapping between 3D coordinates
  DICOM Registration – rigid matrix
  DICOM Deformable Registration
Location of specific points
  DICOM Fiducial
Used to save manual or automated results
  save application state for further work later
  re-use for other purposes (e.g., sync’d scrolling)

## Slide 93: Other Bulk Data Storage
Time-based Waveforms
  ECG
  Hemodynamic
  Audio
MR Spectroscopy
  Single voxel
  Multi-voxel
  Multi-frame
  Metabolite maps (CSI) as images
Raw Data IOD

## Slide 94: Encapsulated PDF Pretty Pictures
A “prettier” alternative to Secondary Capture Images

## Slide 95: All Together Now …
Analysis Workstation
Current DICOM Images from Modality
DICOM Segmentation
DICOM Registration
DICOM SR
DICOM Real World Value
DICOM Parametric Map Images
PACS Store, Distribute and Review
Previous DICOM Images from PACS
Previous DICOM SR etc

## Slide 96: SR as the Organizing Structure
Analysis Workstation
Current DICOM Images from Modality
DICOM Segmentation
DICOM Registration
DICOM SR
DICOM Real World Value
DICOM Parametric Map Images
PACS Store, Distribute and Review
Previous DICOM Images from PACS
Previous DICOM SR etc

## Slide 97: Distributing the Results
Analysis Workstation
Current DICOM Images from Modality
DICOM Segmentation
DICOM Registration
DICOM SR
DICOM Real World Value
DICOM Parametric Map Images
PACS Store, Distribute and Review
Previous DICOM Images from PACS
Previous DICOM SR etc

## Slide 98: Final thoughts …
DICOM is not just for modality vendors
Use of DICOM facilitates faster translation from research into clinical trial and/or clinical use with structured data, not just “pretty pictures”
Research applications can benefit from improved organization in enhanced family images, even if conversion required
Rich family of DICOM objects and mechanisms to support quantitative imaging result recording, derived images, and intermediate results
New parametric map object with floating point pixels
New SR templates and related infrastructure for measurement encoding with rich research-specific code sets and templates
DICOM is responsive to research requirements (e.g., QIICR project, WG18 Clinical Trials & Research) – 9 month cycle time if aggressive
Widely used toolkits can rapidly adopt new mechanisms (e.g., dcmtk in response to QIICR requirements) leading to broader generic support (e.g., in 3D Slicer, Osirix, ClearCanvas, etc.)