## Slide 1: 3D Slicer Tutorial: Prototyping Surgical Robot System Using ROS and 3D Slicer
Junichi Tokuda1, Tobias Frank2,
Axel Krieger3, Simon Leonard4, Niravkumar Patel5
1 Brigham and Women’s Hospital
2 Gottfried Wilhelm Leibniz Universität Hannover
3 Children’s National Health System
4 Johns Hopkins University
5 Worcester Polytechnic Institute

## Slide 2: Background
Growing Interest in Robot Assisted Interventions
  Robot-assisted laparoscopy
  Robotic catheter systems
  Robotic radiosurgery, etc.
R&D of Surgical Robot System
  Image processing and visualization for surgical planning
  Kinematics and motion planning for robot control
  Device management and control
 Requires a wide range of tools and methods developed in robotics and medical image computing fields

## Slide 3: Background (2)
Common research platforms
  Medical Image Computing
    3D Slicer
    MITK
    NifTK
    OsiriX…
  Medical Robotics
    da Vinci Toolkit (dVRK)
    Raven II
    KUKA Lightweight Robot
 Need for a bridge between ROS and OpenIGTLink
Data sharing interface based on OpenIGTLink
Integrated with
Robot Operating System (ROS)

## Slide 4: Objective of This Tutorial
Prototype surgical robot system using widely-available software and hardware
  3D Slicer as planning interface
  Lego Mindstorms as robot hardware
  Robot Operating System (ROS) as robot control software
Through this tutorial, you can:
  Learn software architecture of surgical robot systems
  Acquire hands-on experience of software-hardware integration for medical robotics

## Slide 5: Prerequisite
3D Slicer Version 4.6 or later
Lego Mindstorms EV3 with WiFi dongle
ev3dev – Debian Linux for Mindstorms EV3
  http://www.ev3dev.org
ROS-IGTL-Bridge
  https://github.com/openigtlink/ROS-IGTL-Bridge

## Slide 6: Architecture
Planning Workstation
EV3 Brick with ev3dev
Robot control node
ROS-IGTL-Bridge
3D Slicer
OpenIGTLink
over TCP/IP
ROS
network

## Slide 7: Tasks in Each Compenent
3D Slicer
  Medical Image Display
  Segmentation
  Procedure Planning
  Pre/Intra Image Registration
  Tracker support
OpenIGTLink
  Communication Protocol
  Transformation manager
ROS
  Robot Control
  Path Planning
  Image Libraries
  Sensor Integration
  Simulation
ROS-IGTL-Bridge
  Convert ROS topics to OpenIGTLink
  Transformation manager
Controller Node
  Control actuators

## Slide 8: Step 1: Preoperative Planning
Pre-operative MRI Brain Scan
Mark three distinct points on brain for registration in Slicer
Plan cut in Brain Stem for tumor removal in Slicer

## Slide 9: Step 2: Pre/Intraoperative Registration
Place scalpel over three distinct points for registration
Send registration points through ROS to Slicer

## Slide 10: Step 2: Pre/Intraoperative Registration (2)
Perform registration in Slicer
Send target points for cut to ROS

## Slide 11: Step 3: Robotic Procedure
Robot path is planned and sent to robot
Robotic traces the planned trajectory

## Slide 12: Conclusion
Integration of 3D Slicer and ROS
  Provide access to resources developed in two communities
  Allows quick prototyping of surgical robot systems
  Thanks to a wide variety of hardware supported by ROS, the system can be scaled up easily without changing the system architecture