## Slide 1: DTI Atlas Registration via 3D Slicer and DTI-Reg
Martin Styner, UNC
Guido Gerig, UUtah

## Slide 2: DTI Registration
This tutorial teaches you how
  Load DTI datasets & masks
  Perform a pair-wise registration to a prior atlas via DTI-Reg
    Affine transform and deformable transform
  Save the transformed images and the deformable transform

## Slide 3
Combining information from multiple images requires the geometric relationship between them to be known...
Concept of Registration

## Slide 4
aligned
Concept of Registration: Overlay of pair of images
misaligned

## Slide 5
Transformation for Image Registration
Choice of transformations (complexity of transformation, #degrees of freedom
depends on application).
credit: R. Szelisky, Computer Vision

## Slide 6
3D Transformations
Translation (3 DOF)
Rigid:
Trans & Rot (6 DOF):
Affine (12 DOF)
B-spline (deformable,
grid of control points)
Diffeomorphic (highly deformable,
smooth transformation, invertible)
Linear Transformations (invertible, low DOF):
Nonlinear, deformable transformations (high DOF):

## Slide 7: Co-registration: From linear to nonlinear
Linear registration (affine)
Nonlinear registration (diffeom.)
Example: Registration of DTI to atlas template

## Slide 8: Atlas Building: Averaging registred FA images
raw
linear
nonlinear
Quality (sharpness) of atlas improves with deformable transformations.

## Slide 9: DTI Population Atlases
Definition of standard, normative space
Templates to become available to researchers
Neonate
1 year
2 year
Adult
Rhesus (15mo)

## Slide 10: Spatial Transformations of Diffusion Tensors
Warmer colors indicate higher anisotropy
Principal diffusion directions in anisotropic regions of a DT-MR image slice
James Gee, Department of Radiology University of Pennsylvania

## Slide 11: Rotation without DT Reorientation: Transform voxel grid, leave tensors
  Directional structure is lost.
  DTs orientations are no longer consistent with the anatomical structure of the image.
James Gee, Department of Radiology University of Pennsylvania

## Slide 12: Rotation with DT Reorientation
  DR·D·RT.
  Directional structure preserved.
  DTs orientations remain consistent with the anatomy.
James Gee, Department of Radiology University of Pennsylvania

## Slide 13: Affine Tensor Transformations (Alexander et al, MICCAI 1999)
For an affine transformation, , DF·D·FT?
No...
DF·D·FT
Original Tensor
Transformed Tensor
DR·D·RT
We wish to preserve the shape of the DTs.
But we must reorient them appropriately.
Require R that reflects reorientation due to F.
Decompose F into:
  Rigid rotation, R, and
  Deformation, U: F = R·U R = F ·(FT ·F)-1/2
Then reorient D using R: D’ = R·D·RT
Finite Strain Estimation

## Slide 14: Dataset
For this tutorial you will need DTI data files that can be found following this link : http://hdl.handle.net/1926/1759

## Slide 15: Start Slicer 4
Linux/Mac users :
Launch the Slicer
executable located in
the Slicer4 directory
Windows users :
Select StartAll ProgramsSlicer4.0.1Slicer
Or launch the Slicer executable from Slicer4 directory

## Slide 16: Loading DTI Atlas
Left click on file menu
Left click on Add Volume

## Slide 17: Loading DTI Atlas
Select the AdultAtlas.nrrd volume

## Slide 18: Loading DTI Atlas Mask
Load AdultAtlas_BrainMask.nrrd label map

## Slide 19: Adjust View
Adjust view to see both mask and atlas
Link all 3 viewers
Opacity change
1
2

## Slide 20: Loading 2nd DTI dataset
File Menu =>Add Volume (or see previous tutorial)
Directory: DiffusionDataset_Step2
Load dwiDataset_DTI.nrrd

## Slide 21: Loading DTI dataset mask
File Menu =>Add Volume (or use from previous tutorial)
DiffusionDataset_Step2
Load BrainMask
“LabelMap” checkbox

## Slide 22: Overlay DTI datasets
How can we check alignment?
Overlay the DTI images!
1
2
Select AdultAtlas for Foreground
Set Opacity to 0.5

## Slide 23: Overlay
Bad alignment: 2 separate corpus callosum

## Slide 24: Select DTI-Reg Module
Slicer modules
  Diffusion
  → Utilities
  → DTI-Reg
DTI-Reg: Pairwise DTI registration module
Notes: Under Welcome to Slicer
Go to Diffusion
Utilities -> DTIreg

## Slide 25: Volumes for Registration
Fixed Volume: Target of registration = AdultAtlas.nrrd
Moving Volume: Image to be transformed: dwiDataset_DTI
1
2

## Slide 26: Set Masks for Registration
Set Fixed Mask to Atlas Mask: AdultAtlas_BrainMask.nrrd
Set Moving Mask to dwiDataset Mask: dwiDataset_BrainMask.nrrd
1
2

## Slide 27: Set Transform to Affine
Set registration transform to Affine
Deformable Registration is performed in 2 steps: Affine followed by nonlinear.
ANTS generally better but much slower

## Slide 28: Select Outputs
Create & rename volumes for output
Affinely registered DTI dataset
Affine transform
Apply to run & wait
1
2

## Slide 29: Registration
Several pairwise registration methods available.
DTI-Reg supports several registration methods based on normalized FA images:
    Affine, B-spline, Demons-variants from within Slicer
    ANTS as external call
Plan: DTI-TK support
  Registration based on full tensor.

## Slide 30: Affine Results
Select DTI-Reg result as background
Result: single corpus callosum, but fuzzy, insufficient registration

## Slide 31: Deformable Registration
Concept: Use affine registration as initialization for deformable registration:
Change moving volume to affinely registered data
Change moving mask to atlas mask
Change registration to Diffeomorphic (Demons)
Create/rename output names for deformable transformation
1
3
5
2
4

## Slide 32: Deformable Results
Select DTI-Reg deformable result as background
Result: No longer fuzzy, significantly better registration

## Slide 33: Save Outputs and Done
Save selected volumes and transforms
File → Save → (deselect/select checkboxes)
Choose common directory: “destination for all selected”

## Slide 34: Conclusions
DTI registration is available in Slicer
2-step process currently, to be improved soon
Brainmasks are needed (unless data is skull stripped already)
This tutorial taught you how to register to an atlas
  How to get atlas?
Alternative: Build atlas from data

## Slide 35: Acknowledgment
National Alliance for Medical Image Computing NIH U54EB005149
UNC: Jean-Baptiste Berger, Clement Vachet, Aditya Gupta
Utah: Guido Gerig, Sylvain Gouttard
Iowa: Hans Johnson, Joy Matsui